General Department of Legal Affairs and International Cooperation

Legal Affairs

Draft Implementing Regulations for the Law of Explosives and Fireworks

Issued by the Royal Decree No. 38 Dated 28/04/1428 AH

Section One

Definitions

Article One:

The following terms and expressions, wherever they may occur in the present Regulations, shall have the meanings respectively indicated below, unless the context indicates otherwise:

1. Law: Law of Explosives and Fireworks Issued by the Royal Decree No. 38 Dated 28/04/1428 AH.

2. Explosives: Chemical compound or mixture that turns very quickly, when exposed to external influence, into quantities of gas, high temperature and great pressure because of the chemical reaction producing a crushing power to everything around it.

3. Fireworks: Chemical compounds or mixture that are made to make bang sounds with halos and light or smoke forms such as (luminous or smoky fireworks intended for use at festivals and events).

4. Licensed: The natural or legal person who meets the necessary conditions and has permission from the Ministry.

5. Minister: Minister of the Interior.

6. Ministry: Ministry of Interior.

7. Authority: Governmental or non-governmental entities and institutions.

8. Commission: The High Commission for Industrial Security.

9. Permanent Committee: The committee that is formed from the following authorities: The Department of Weapons and Explosives at the Public Security, The General Investigation, The General Department of Weapons and Explosives at the Ministry and The High Commission for Industrial Security.

10. Regulations: The Implementing Regulations for this Law.

Section Two

Names, Types and Related Items of Explosives and Fireworks

Based on Article 3 of the Law, which states that the Regulations shall specify the names, types, related items and necessary supplements of Explosives and Fireworks.

Chapter One

Names, Types and Related Items of Civilian and Petroleum Explosives

Article Two:

Types of explosive materials:

1. Emulsion explosives.

2. ANFO explosives.

3. Seismic explosives.

4. Electric detonators.

5. Non-electric detonators.

6. Detonation cords.

Article Three:

Names of commercial explosive materials:

1. Chemolex - Nitram - Xplus (Emulsion explosives).

2. Brilex - Nitro - Nitral (ANFO Explosives).

3. In viruses (Seismic Explosives).

4. Locally manufactured explosives which are approved periodically by the General Department of Weapons and Explosives at Public Security according to what develops in this field.

Article Four:

Related items of explosives:

1. Explosive device.

2. Geophone.

3. Blasting mats.

Article Five:

Types of petroleum explosives:

1. Cartridge.

2. Drillers.

3. Detonator.

4. Tube cutter.

5. Stuffing.

6. Ignition device.

7. Additional fuse (booster).

8. Detonation wire.

9. Detonation primer.

Chapter Two

Names, Types and Related Items of Fireworks

Article Six:

Types of fireworks:

1. Luminous.

2. Sound.

3. Smoky.

4. Fiery.

Article Seven:

Names of commercial fireworks:

1. Separate missile.

2. Fountains.

3. Volcanoes.

4. Roman candle.

5. Waterfall.

6. Flashes.

7. Fireworks which approved periodically by The General Department of Weapons and Explosives at the Public Security according to what develops in this field.

Article Eight:

Related items of fireworks:

1. Batteries.

2. Launchers.

3. Means of ignition.

4. Slow flaming fuse.

5. Electric connection wires.

6. Electronic ignition system.

Chapter Three

Flares and Safety

Article Nine:

Names of flares and safety:

1. Flare gun.

2. Fire extinguisher vessel.

3. Float blowing valve assembly provided with two squibs.

4. Detonation cartridge assembly.

5. Fire extinguisher cartridge.

6. Repair kit.

7. Air flare shot.

8. Cable cutter with cartridge.

9. Ignition float valve.

10. Grey smoke cylinder.

11. Flare shot.

12. Car warning flare.

13. Hand red flare.

14. Marine parachute rocket red flare.

15. Floating smoke orange flare.

16. Mobile rescue line launcher.

17. Smoke flare and automatic lighting for a person in the middle of the sea.

18. Floating smoke flare for a person in the middle of the sea.

19. Hand flare.

20. Projectile flare.

21. Floating smoke flare.

22. Cord launcher.

23. Luminous flare with smoke.

24. Periodically approved flares by The General Department of Weapons and Explosives at the Public Security according to what develops on this field.

Section Three

Manufacture of Explosives

Based on Articles 4 and 6 of the Law, which states that the manufacture of explosives is prohibited except with an authorization from the Ministry, and the authorized person shall organize special records in accordance with the forms and procedures specified by the Regulations.

Chapter 1

License

Article Ten:

Conditions for requesting license to manufacture explosives:

1. The applicant for license shall be a company owned with at least 51% (present) by a Saudi partner(s) having the right of management, or the applicants shall be individuals who are in the process of establishing a commercial entity with the same proportion.

2. The founder(s) of natural persons shall not have been sentenced for immoral behavior and breach of trust offense.

3. The license applicant shall determine who would run the company on the condition that he shall be a Saudi citizen with good conduct.

4. The applicant shall have the financial capacity to meet the requirements of this activity and the establishment of factories and warehouses so the investor's capital shall be at least 20 million SAR.

5. The applicant shall provide a bank guarantee of one million SAR for the Ministry from a local bank valid for five years.

6. He shall provide a comprehensive economic feasibility study of the project issued by a competent authority that includes the project-estimated budget, the products to be manufactured, the expected production capacity, the required equipment and devices for manufacture and the target clients.

7. Provision of trucks with special specifications to transfer explosives after manufacture.

8. Develop training courses and awareness programs on a regular basis related to the safety of handling explosives.

9. Provision of an electronic, computer and book system that can control the stock, knows the incoming and outgoing products, and traces that automatically in accordance with the Public Security requirements.

10. Providing insurance coverage for damages caused by accidents related to practicing this activity or those inflict on others.

11. Providing any information, data or documents that the Ministry believes it is necessary to examine the request.

12. The Ministry shall have the right to amend the conditions and rules for practicing this activity whenever it called for the security interest without any responsibility the Ministry may have.

Article Eleven:

Procedures for obtaining a license to manufacture explosives:

1. The license request shall be submitted to the Ministry represented by the General Department of Weapons and Explosives attached by the following:

a. A true certified copy of the natural persons founders' IDs, their addresses, contact numbers and any commercial activities if any.

b. A copy of the commercial register and the incorporation contract if any.

c. A true certified copy of the ID of the one who will manage the company and a summary of his administrative and technical experience related to the explosives manufacturing activity.

d. A written declaration stating that the applicant acknowledges the conditions and rules for practicing this activity and pledges to comply with them.

2. The request shall be examined by the Permanent Committee to ensure that it meets all the required conditions, and then it shall submit its recommendations to the Minister with the initial approval or rejection. A copy of the decision shall be provided to the Ministry of Commerce and Industry to complete the registration and establishment procedures according to the regulations of the Ministry of Commerce.

3. The Commission shall be provided with a copy of the decision after the initial approval to coordinate with the applicant to select the right location for establishing the explosives factory.

4. The Commission shall supervise the engineering sketches of the project by an approved engineering office.

5. The Commission shall supervise the security clearance for contractors who are working on security systems, safety and fire protection systems and following up construction works. It shall ensure that the security requirements are met by the explosives factory.

6. After completing the project, the Permanent Committee shall ensure that it meets all conditions and requirements, and then submit its recommendation to the Minister to issue the final approval of the license request.

7. The license shall be issued by a ministerial decision and lined with the activity in a specific location and a similar license shall be obtained in case of expanding and practicing the activity in another location.

8. The final license shall be valid for five years and renewed for a similar period whenever the licensee follows the rules governing the activity. If the license is lost or damaged, it shall be replaced by the remaining period including the same information with the same issuance fees.

9. If the ownership of the facility or company is transferred in whole or in a part, the license shall be renewed with the same conditions within three months and it shall be considered terminated unless a renewing request is submitted during this period.

10. The ongoing companies practicing the activity of manufacturing explosives shall be obligated to reform their status by applying to the Ministry represented by the General Department of Weapons and Explosives to obtain a license issued by a ministerial decision similar to new factories.

11. The Ministry may terminate the license in case that the applicant does not comply with the conditions and rules specified in the Regulations or whenever the security interest requires that.

Chapter Two

Factory Location

Article Twelve:

Conditions for explosives factory locations:

1. The location shall be far from city borders with a safe distance determined by the Permanent Committee.

2. The location shall be far from Saudi Arabia borders with a safe distance determined by the Permanent Committee.

3. The location shall be far from the train tracks and highways with a safe distance determined by the Permanent Committee.

4. The location shall be far from the petroleum facilities, oil and gas pipelines, dams, irrigation and sewage pipes, water pipes and desalination and electricity stations with a distance not less than 5 kilometers or as determined by the Permanent Committee.

5. The location shall be far from radio and television transmitting station towers, military and civilian communication towers and power transmission towers with a safe distance determined by the Permanent Committee.

6. The location shall not be in the ongoing nature reserves in Saudi Arabia as determined by the Permanent Committee.

7. The location shall not be within the exclusive locations of oil, gas or mining except with the approval of the Ministry of Petroleum and Mineral Resources.

8. The location shall be flat and not exposed to drifting of sand.

9. The location shall not be in water streams, water springs or low-lying areas that are exposed to flooding.

10. A good dirt road shall ease for all types of vehicles to arrive at the location.

11. The area of the location shall not be less than 1 million square meters or as determined by the Permanent Committee.

12. The location shall be surrounded by a sanctuary or security distance as determined by the Permanent Committee.

Chapter Three

Security Requirements and Rules

Article Thirteen:

Security requirements that shall be met by the explosives factories:

1. Build a security fence surrounding the factory location according to the Commission's standards.

2. Install vehicle assault barriers outside the security fence according to the Commission's standards.

3. The factory and warehouse area shall be a prohibited area and separated with a security fence from the administrative and service area.

4. Build a road for security patrols inside and outside the security fence.

5. Make a security sanctuary inside and outside the fence with a width not less than 15 meters.

6. Provide a security distance not less than 60 meters between the security fence and sensitive facilities that are located inside such as warehouses and power stations.

7. Build a main gate to enter the administrative and service area of the factory.

8. Build a gate to enter the prohibited area (factory and warehouses) taking into consideration the following:

a. The gate shall be designed with an entry lane, exit lane and a guardroom between the two lanes.

b. Build the lower part of the guardroom wall from reinforced concrete and the upper part from bulletproof glass on all sides.

c. Install sliding doors to close the gate when needed.

d. Install hydraulic road blockers and automatic boom barriers in both entry and exit lanes. They shall be automatically controlled by smart cards and fingerprint.

e. Install a under vehicle scanning system in the entry lane.

f. Install automatic revolving doors to control the entry line of individuals.

g. Provide the staff entrance gate with metal detectors.

h. Install rotating colored cameras to monitor entry and exit movement.

9. Make an emergency gate on the fence of the prohibited area equipped with hydraulic road blockers.

10. Provide gates with wired and wireless communication devices and hotlines to be used by the security guards in charge of inspection and guarding.

11. Provide lights along the security fence surrounding the site, gates, factory interior areas and warehouses according to the High Commission for Industrial Security standards.

12. Install an integrated electronic security system in the whole factory area and interior sensitive facilities. It is operated by a central control and surveillance room and includes, for example, infiltration detection systems and CCTV cameras.

13. Establish an industrial security department and provide all necessary equipment, buildings and qualified personnel.

14. Inspect all workers and visitors without exception upon entry and exit.

15. Provide the necessary number of Industrial Security officers in charge of guarding after the Ministry's approval. They shall be deployed according to a unit structure determined by the Commission.

Article Fourteen:

Rules of the activity of explosives manufacture:

1. The manufacture shall be for specific types of explosives intended for civilian use. It is not allowed to produce other unlicensed types except for experiments in coordination with Public Security.

2. Prepare an annual program, in coordination with the Public Security, that includes the materials to be produced, its quantities, forms and packaging specifications. It is not allowed to increase production except with the Public Security's permission.

3. Comply not to modify the produced substance nature, characteristics, size, form or packaging specifications except when licensed.

4. A digital tracking system shall be used on the cover of each produced unit that enables to control the movement of materials at the time of release, storage and confirm the validity date in coordination with the Public Security.

5. Comply to submit a monthly statistical statement to the Public Security that shows the produced, sold and remaining quantities of explosives.

6. Follow up the raw materials released for manufacturing operations and the resulting materials, and register that in special records that are ready for auditing and reviewing upon each request.

7. Do not use the raw materials mixing trucks to manufacture explosive materials at the fieldwork locations without the Public Security's approval and supervision.

8. Provide the Public Security with a list of the workers' names in the production line and those whose work is related to seizing and transporting explosives, their jobs, places of work, places of residence and nationalities. This shall be updated regularly.

9. The factory shall be managed by a Saudi person who is efficient, administratively and technically experienced and familiar with this activity. He shall be assisted by a Saudi administrative employee on site who meets the same conditions.

Section Four

Import of Explosives

Based on Articles 4, 6 and 10 of the Law, it is prohibited to import explosives except with the Ministry's permission, and the licensee shall organize special records according to the forms and procedures determined by the Regulations. Conditions, procedures, technical and security specifications, and safety requirements shall be specified upon importing explosives.

Chapter One

License

Article Fifteen:

Conditions for requesting an import license for explosive materials:

1. The applicant shall be one of the following categories:

a. Those licensed to manufacture explosives have the right to import explosives that are fully manufactured in case that they are unable to manufacture it locally due to the lack of economic and technical feasibility, techniques or components that are difficult to be manufactured locally.

b. Those who are licensed by the Ministry of Petroleum to work in the field of oil and gas exploration provided that importing the explosives shall be related to their activities.

c. Those who are licensed by the Ministry of Agriculture to work in the field of water deep well drilling provided that importing the explosives shall be related to their activities.

d. Those who are licensed to supply rescue and safety equipment and tools and want to import relief and maritime rescue equipment containing explosives such as flares.

2. Provide a bank guarantee with an amount of two hundred thousand SAR issued for the Ministry from a local bank valid for five years.

3. The applicant shall have the financial capacity to build legal warehouses according to the conditions specified by the Regulations.

4. Provide legal warehouses to store explosives according to the requirements of the present Regulations.

5. A work plan with details shows how the project is operated and the volume, types and quantities and country of origin of the explosives to be imported.

6. Provide special trucks to transport explosives according to the specifications determined by the present Regulations.

7. Provide an electronic system to automatically control inventory, know incoming and outgoing and track each imported item.

8. Comply to provide any information, data or documents that the Ministry deems necessary to examine the request.

9. Acknowledge that the Ministry has the right to amend conditions and rules to practice this activity whenever the security interest requires that.

10. Provide insurance coverage for the damages caused by accidents related to practice this activity or inflict on others.

Article Sixteen:

Procedures for obtaining a license to import explosives:

1. The license application shall be submitted to the Ministry represented by the General Department of Weapons and Explosives attached with the following:

a. A true certified copy of the establishment owner's ID or the founders of the said company, their addresses, contact numbers and commercial activities if any.

b. A true certified copy of the commercial register and the incorporation contract.

c. A true certified copy of the identity of the person who will manage the project, and a summary of his administrative and technical experience in this field.

d. A written declaration stating that the conditions and rules for practicing the activity are acknowledged and complied with.

e. A letter of support from the Ministry of Petroleum and Mineral Resources in case that the applicant is one of the operating institutions or companies in the field of oil and gas.

2. The Permanent Committee shall study the request to ensure that it meets all the required conditions, and then submit its recommendation with initial approval or refusal to the Minister for approval.

3. The Public Security shall be provided with a copy of the initial approval to coordinate with the applicant to choose a suitable location to construct the warehouses.

4. The Public Security shall supervise the engineering sketches to construct the warehouses by an approved engineering office.

5. The Public Security shall supervise the follow-up of construction work and ensure that it conforms to security specifications.

6. After completing the construction of the warehouse, the Permanent Committee shall check that all conditions and requirements are met and submit its recommendations to the Minister in preparation to issue the final approval on the license request.

7. The license shall be issued by a ministerial decision which is valid for a period of five years and renewed for a similar period whenever the licensee complies with the rules regulating this. If the license is lost or damaged, it shall be replaced by the remaining period including the same information with the same issuance fees.

8. If the ownership of the facility or company is transferred in whole or in part, the license shall be renewed according to the same conditions to be granted within a period of three months. The license shall be considered terminated unless a renewal request is submitted during this period.

9. The ongoing companies practicing the activity of explosives importing shall comply to submit a request to reform their status to the Ministry represented by the Public Department of Weapons and Explosives to obtain a license issued by a ministerial decision similar to new companies.

10. Facilities and companies working with the Ministry of Petroleum and Mineral Resources are not required to construct permanent warehouses in case that the Ministry of Petroleum and Mineral Resources or its subsidiaries are committed to construct them in accordance with the requirements set by the present Regulations.

Chapter Two

Activity of Import

Article Seventeen:

Rules for the activity of explosives importing:

1. The licensed in explosives import activity shall apply for import permit from the Ministry represented by the Public Security, in which he clarifies the annual need for explosives, specified in quantity, type, category and country of origin.

2. The request shall be submitted to the General Department of Weapons and Explosives at the Ministry after being examined by the Public Security and the necessary procedures are completed.

3. The Minister shall issue the import permission indicating the types, categories and quantities. It shall be valid until the end of the Hijri year and can be exploited by partial import of quantities in separate shipments throughout the year.

4. The importer shall inform in writing the concerned regional police before starting to import each shipment within a period of not less than two weeks. The report shall include the types, categories, quantities contained in the shipment, country of origin, port of entry, carrier, means of transport and date and time of the shipment arrival. In addition, it determines the location and capacity of the warehouse in which explosives are stored.

5. The concerned regional police shall issue the clearance permit directed to the Customs of the port of import in the light of the written notice, including all the information contained in the notice, and all the relevant security authorities shall be notified.

6. Explosive materials shall be inspected before they are released, with the participation of a representative from the regional police, Customs and other authorities specialized in importing explosives, at the port of arrival to ensure the quantity, types and categories of incoming explosives and their conformity with the clearance permit, and then prepare a report on that.

7. If it turns out that there are types, categories or quantities that are not identical to the importation clearance permit, the importer is obligated to return them to the source or destroy them at his expense.

8. It is not permissible to leave the explosives at the port of arrival and they shall be transported immediately after being cleared by trucks designated to transport explosives provided by the importer and under the guard of the regional police until they arrive at the storage warehouses, and then received and added to the importer's balance according to an entry record.

9. The importer may not sell the imported items or use them for purposes other than the purpose of import except with the Ministry's approval.

10. The importer shall instruct the exporting authority to prove the production date and validity period on the imported materials.

11. The importer shall keep a record to write the names of his workers in the field of direct import of explosives, their jobs, places of residence and nationalities, as well as places to store explosives, worksites to which they are transported, quantities and dates of their transfer.

12. The importer shall submit a monthly statement to the Public Security stating the types and quantities imported, sold, consumed or remaining.

Section Five

Export of Explosives

Based on Articles 4, 6 and 10 of the Law, it is prohibited to export explosives except with permission from the Ministry, and the licensee shall have special records according to the forms and procedures specified by the Regulations. The conditions, procedures, technical and security specifications, and safety requirements shall be specified when exporting explosives.

Chapter One

License

Article Eighteen:

Conditions for explosives export request:

1. He shall be licensed to manufacture explosives and be practicing this activity for a period of no less than three years.

2. The export shall be of surplus production after covering the local market needs.

3. Providing trucks authorized to transport explosives to the port of export.

4. Providing an electronic system, in coordination with the Public Security, through which it can monitor inventory, know the incoming and outgoing automatically, and track the movement of items.

5. Providing a bank guarantee of fifty thousand Saudi Riyals issued in favor of the Ministry from a local bank, valid for a period of three years.

6. Providing insurance coverage for damages resulting from accidents related to the explosives export activity or that inflict on others.

7. Providing any information, data or documents that the Ministry deems important to study the request.

8. Acknowledgment of the Ministry's right to amend the conditions and rules for practicing the explosives export activity whenever the security interest requires that.

Article Nineteen:

Procedures for obtaining a license to export explosives:

- The license request shall be submitted to the Ministry represented by the Public Department of Weapons and Explosives.

- The following shall be attached to the license request:

- A copy of founders or owners' IDs, along with their CVs, addresses, contact numbers, and commercial activities, if available.

- A copy of the commercial register and the company incorporation contract.

- A copy of the license to manufacture explosives and the actual date of the manufacturing activity.

- A copy of the ID of the person who will manage the project and a description of his administrative and technical experience in this field.

- A written declaration stating that the applicant has reviewed the conditions and rules for the explosives export activity and abiding by the commitment.

- The request shall be examined by the Permanent Committee to ensure that it meets all the required conditions, and then submits its recommendation with initial approval or refusal to the Minister for approval.

- The license shall be issued by a ministerial decision and valid for a period of three years and renewed for a similar period whenever the licensee complies with the rules regulating the explosives export activity. In case that the license is lost or damaged, it shall be replaced for the remaining period, including the same information with the same fee for the issuance.

- If the ownership of the facility or company is in whole or in part transferred, then the license shall be renewed according to the same conditions for granting within a period of three months. The license shall be considered terminated unless a request for renewal is submitted during this period.

Chapter Two

Activity of Export

Article Twenty:

Rules of export activity of explosives:

- The licensee to practice the explosives export activity shall apply for export permission from the Public Security, indicating the quantities, types, and items, the export port and the beneficiary before starting the export.

- Obtaining approval to export explosives from the concerned authorities in the destination country and certified by Saudi Arabia's representation in that country.

- The request shall be submitted to the General Department of Weapons and Explosives at the Ministry after being studied by the Public Security and completing the necessary procedures.

- The export permit shall be issued by the Minister, indicating the types and categories, and communicated to the concerned regional police. It is valid until the end of the Hijri year and can be used for partial export of quantities and in the form of several shipments throughout the year.

- The exporter shall submit a written notice to the regional police of the region where the explosives will be moved from before the start of the process of exporting each shipment for a period of not less than two weeks, including the contents of the shipment, quantities, types and items in addition to specifying the location of the exportation port and the warehouses which the explosives will be moved from.

- The regional police shall coordinate with the exporting company to determine the appropriate time and date to transport the shipment, issue an exportation clearance permit to the exportation port Customs, and notify the International Communication Police and the regional police in which the exportation port is located.

- The regional police from which the explosives will be moved shall be responsible for moving the explosives from the warehouses and escorting the materials transported under security guard to the exportation port.

- The transported materials shall be received by the Customs and regional police in which the port of export is located, and a report shall be prepared for this after making sure that the quantities, types and items are in compliance with the exportation clearance permit.

- The arrival of the materials transported by land to the port of export shall be done during the day so that the process of receiving and delivery between the two border ports can be completed and that the transported materials are not kept without security guard until they are provided from the other side.

- The licensee to export explosives shall submit a monthly statement to the Public Security indicating the types, items and quantities that have been exported, as well as the export destination.

- It is not permissible to export what has been imported from fully manufactured explosives unless they are complementary to locally produced materials or with the Minister's approval.

Section Six

Storage of Explosives

Based on Articles 4 and 10 of the Law, it is prohibited to store explosives without a license from the Ministry. The stipulated conditions, procedures, technical and security specifications and safety requirements shall be met when storing explosives as well as in storage warehouses as specified.

Chapter One

Warehouses

Article Twenty-One:

Types of warehouses:

- Central warehouses (main):

It is constructed by producing companies at the factory location in order to store what is produced or imported of explosives with a capacity not exceeding 500 tons.

- Sub-warehouses:

It is constructed by the producing companies outside the factory location at a distance of not less than 300 km for the purpose of distribution with a capacity not exceeding 300 tons.

- Permanent warehouses:

It is constructed by companies or establishments that use explosives in long-term projects such as mining, cement and oil projects. The accommodation capacity shall not exceed 300 tons.

- Temporary warehouses:

The warehouses that are constructed for a non-permanent purpose and are used by companies or establishments to serve short-term projects such as construction projects, roads, and drilling of water wells, and can be removed at the end of the project and their capacity not exceeding 55 tons.

- Underground warehouses:

They are constructed by mining companies operating in underground mines for supplying explosive materials near workplaces and are supplied from permanent warehouses in quantities that allow continued work for short periods.

- Drilling pipes processing workshop warehouses:

They are constructed by oil and gas companies in workshops in which drill pipes are loaded with explosive materials and are supplied from permanent warehouses in quantities that allow work to continue for short periods.

Article Twenty-Two:

Conditions for warehouse locations:

- Central warehouses: these warehouses shall meet the same requirements for an explosives factory location.

- Sub and permanent warehouses:

- The site shall not be within the oil, gas or mining exclusive sites without the approval of the Ministry of Petroleum and Mineral Resources.

- The site shall be far from the city borders at a safe distance, as determined by the Permanent Committee.

- The site shall be far from the borders and beaches sanctuary at a safe distance, as determined by the Permanent Committee.

- The site shall be flat and not exposed to the movement of drifting sand.

- The warehouses shall not be built in valleys, low-lying areas and water springs.

- Easy access to the site shall be provided through two roads, one of which is paved with asphalt.

- The site shall be far from petroleum facilities, oil and gas pipelines, at a safe distance, as determined by the Permanent Committee.

- The site shall be far from dams, irrigation and sewage canals and water pipes with a safe distance, as determined by the Permanent Committee.

- The site shall not be adjacent to radio and television transmitting towers, military and civilian communication towers, airports and high-pressure power towers.

- The site shall not be located in nature reserves in Saudi Arabia or adjacent to it.

- Temporary warehouses:

- They shall be away from urban areas by a distance of not less than 20 km depending on the geographic features, and according to what the Weapons and Explosives Department at the regional police deems appropriate.

- The location shall be far from public facilities and services such as main roads, water lines, oil and water resources by a distance of not less than 10 km based on the geographic features, or as determined by the Weapons and Explosives Department at the regional police.

- The site shall be far from power lines and high-pressure power by a distance of not less than 5 km, depending on the nature of the place.

- If the land on which the warehouse will be built is owned by a government entity, official permission shall be obtained from that authority to allow the construction.

- If the land on which the warehouse will be built belongs to a private entity, whether legal or individual, it is necessary to provide the competent authority with a copy of the lease contract and a copy of the property deed. Provided that the contract period is not less than the project implementation period.

- The road leading to the location shall be easy to take and not be obstructed by valleys or water streams, provided that there is an alternative road leading to the same location.

- Constructing warehouses in valleys and water stream channels is not allowed.

- It shall not be close to nature reserves and pastures by a distance of no less than 5 km, depending on the geographic features, or as determined by the Weapons and Explosives Department at the regional police.

- The site shall be far from the sea coasts by a distance of not less than 15 km, depending on the geographic features, or as determined by the Weapons and Explosives Department at the regional police.

- It shall be far from border areas and the border sanctuary by a distance of not less than 20 km, based on the geographic features, and what the specialists deem appropriate.

- Processing warehouses:

- The site shall not be previously allocated to a government or private entity with approved justifications unless the concerned entity agrees.

- The site shall be far from the city borders at a safe distance determined by the Permanent Committee.

- It shall be far from the border sanctuary of Saudi Arabia by a safe distance determined by the Permanent Committee.

- The site shall be far from train tracks and public roads at a safe distance determined by the Permanent Committee.

- The site shall be far from petroleum facilities, oil and gas pipelines, dams, irrigation and drainage canals, water pipes, desalination and power plants by a distance of no less than 5 kilometers, or as deemed by the Permanent Committee.

- The site shall be far from radio and television transmitting towers, military and civilian communication towers, and high-pressure power towers at a safe distance determined by the Permanent Committee.

- The warehouse shall not be located in nature reserves in Saudi Arabia, as determined by the Permanent Committee.

- The warehouse territory shall be flat and not exposed to the drifting of sand.

- The site shall not be in water streams, water springs, or low-lying areas.

- A well-paved road that facilitates access for all vehicle types shall be built.

- The warehouse shall be surrounded by sanctuary or security distance as determined by the Permanent Committee.

Article Twenty-Three:

Technical and security specifications for constructing main, sub and permanent warehouses:

- The walls shall be built with concrete bricks with a thickness of not less than 20 cm or reinforced concrete with a thickness of not less than 15 cm and a height of not less than 3 meters. They shall be smooth and not have sharp corners. The walls, floors and ceilings of the building shall be made of fire-resistant materials for two hours.

- The floor shall be of reinforced concrete with a thickness of not less than 10 cm, and covered with a smooth layer that prevents sparks and easy to clean.

- The roof shall be less solid than the walls, tightly closed and easily detached in the event of an explosion.

- The door shall be made of steel iron with a thickness of not less than 6 mm and covered from the inside with wood of a thickness of not less than 5 cm. The width shall not be less than 140 cm and height not less than 220 cm. It shall be opened to the outside and has two locks, each has a different key.

- The lighting and ventilation shall be natural, and the warehouse shall be free of electrical wiring.

- The roof of the warehouse shall be provided with a protective sunshade against sun and rain, and it shall be painted white and wider than the walls in order to cover them.

- Windows shall be covered from the outside with a strong iron grill and their numbers are sufficient and designed in a way that prevents direct sunlight.

- A lightning mast shall be installed on the top of each warehouse with a round edge and 4 meters high and a diameter of three-eighths. 66 mm copper wires shall connect the mast to well-anchored bases in the ground to a depth of at least 2 feet.

- Each warehouse shall be equipped with a thermometer and hygrometer.

- The detonator warehouse shall be equipped with shelves made of wood or reinforced plastic that are well fixed and separated from the warehouse walls by a distance of 90 cm and a height of about 180 cm.

- Each warehouse shall be equipped with an alarm system and a fire detector associated with the surveillance room, as well as a sufficient number of fire extinguishers, sand buckets and a fire hose reel.

- The safety distances within the warehouse area between each warehouse and the other shall not be less than 50 meters.

- Each warehouse shall be surrounded by an earthen berm of 5 meters away from the walls and the height is 75% of the height of the warehouse with a sufficient distance in front of the door.

- A loading and unloading stage shall be built that allows easy handling from the truck to the warehouse floor, taking into account that there is sufficient distance for the truck to turn and exit.

- Install lighting poles inside the fence, whose lighting is directed to the outside, so that the distance between each pole and the other does not exceed 10 meters.

- The warehouse area shall be surrounded by barbed wire fencing installed on concrete pillars with a height of not less than 2 meters, with a spiral wire installed at the top and bottom of the fence.

- Warning signs shall be placed on the warehouse walls in both Arabic and English (Danger, No smoking, Do not use wired and wireless devices, No open flames). A (No Approaching) sign shall also be placed on the road leading to the warehouse area, with a distance of no less than 100 meters.

- A guardroom shall be built at the warehouse entrance but outside the fence, equipped with means of communication and television surveillance to inspect and prevent the entry of lighters, mobiles and other devices into the storage area, and prevent the entry of unauthorized persons.

- Observation towers shall be built at different sites suitable for surveillance.

- Electricity shall be provided in addition to a backup generator placed in a room outside the warehouse fence.

- The warehouse area shall be easily accessible through two paved roads, and take into account that one of them shall be asphalted.

- It should be taken into consideration that the number and size of warehouses in the storage area are commensurate with the required capacity.

- The Ministry shall have the right to amend the requirements and specifications of warehouses whenever the security and safety requirements so require.

Article Twenty-Four:

Technical and security specifications to construct temporary warehouses:

- It shall be an iron container made of tinplate not less than 5 mm thick and firmly fixed on concrete bases 30 cm above the ground.

- The height of the inside of the container is not less than 240 cm, and the internal walls, ceiling and floor shall be covered with heat-insulating and fire-resistant wood with a thickness of not less than 30 mm.

- They shall be provided with suitable openings for ventilation, covered with a steel iron grill.

- The container door shall be of the type that opens to the outside and has two locks, each with a different key.

- Masts must be installed to prevent lightning.

- The roof shall be weak to absorb the explosive wave if it occurs and be provided with a pyramidal sunshade to protect from the sun and to drain rainwater.

- Each warehouse shall be equipped with a thermometer and hygrometer.

- The lights and ventilation shall be natural so that the warehouse is free of electrical wiring.

- The warehouse shall be provided with a sufficient number of fire extinguishers and sand buckets.

- The safety distance within the warehouse area between each warehouse and the other shall not be less than 20 meters.

- An earthen berm shall be made around each warehouse whose height shall not be less than two-thirds of the warehouse height.

- A security grill fence shall be placed surrounding the warehouse area, at a height of not less than 2 meters, with a spiral wire installed at the top of the fence.

- Install lighting poles inside the fence but the lighting shall be directed to the outside, and the distance between each pole and the other does not exceed 10 meters.

- Provide an electric generator and a backup one to be placed outside the fence.

- Easy access to the warehouse area shall be provided through a paved road.

- Build a guardroom at the warehouse entrance but outside the fence.

- It shall be taken into consideration that the warehouse number in the storage area is proportional to the required capacity.

Article Twenty-Five:

Technical and security specifications for the construction of underground warehouses:

- The rocks surrounding the cavity in which the warehouse is located shall be of a solid type that prevents collapses.

- Support the roof of the warehouse with cement spray and iron pillars to protect from cracks and falling rocks.

- The floor of the warehouse shall be smooth and painted with an insulating material.

- Built ground drainage canals around the warehouse perimeter.

- Close the warehouse front area with a strong iron grill including a door that opens to the outside, not less than 2 meters wide and high, and equipped with two locks.

- Put warning signs on the warehouse fence.

- Provide a ventilation system that allows air circulation over time and an automatic extinguishing system.

- The lighting shall be sufficient, and the electrical wiring and lamps shall be of the safe type for use.

- Provide safety means such as fire extinguishers, sand buckets and backup water tanks.

- Install a security system (surveillance cameras) around and inside the warehouse linked to the external surveillance room.

Article Twenty-Six:

Technical and security specifications for the construction of warehouses attached to drilling pipes processing workshop:

- The warehouse shall be attached to a workshop for preparing drill pipes and built of bricks of not less than 25 cm thickness.

- The area of the warehouse shall not exceed 12 square meters.

- The warehouse door shall be made of steel iron, have two locks, and open to the outside.

- The warehouse floor shall be painted with an insulating material that prevents sparks.

- The electrical wiring shall be in-wall and hidden, and the light bulbs shall be of the safe type.

- Provide an automatic fire extinguishing system in the processing workshop area.

- Place wooden or plastic shelves designed with partitions to allow arranging the stored items.

- Install security systems in the processing workshop area, such as night surveillance cameras, and link them to the security authorities specified by the Ministry.

Chapter Two

Procedures for obtaining warehouse licenses:

Article Twenty-Seven:

- Central warehouses:

These warehouses do not need special licenses as they are attached to factories that are approved through procedures for explosives manufacturing licenses.

- Sub and permanent warehouses:

- The license request shall be submitted to the Ministry represented by the Public Security (the regional Weapons and Explosives Department).

- The Permanent Committee shall study the request and inspect the site on the spot to ensure that it meets all the required conditions, owned by the applicant and the location coordinates are determined.

- When the construction is completed, the committee shall ensure that the warehouse complies with the technical requirements. It shall provide guards, a warehouse keeper and his assistant then submit recommendations to the Public Security director to approve the license request.

- The license shall be issued by the Public Security director and be valid for four years.

- Temporary warehouses:

- The license shall be submitted to the Ministry represented by the Public Security (the regional Weapons and Explosives Department).

- The request shall be examined by a committee formed by a representative of the Weapons and Explosives Department of the regional police and a representative of the regional Investigations Department to ensure that it meets all the required conditions. The committee shall inspect the site on the spot to ensure that it meets all the required conditions.

- When the construction is completed, the committee shall ensure that the warehouse complies with the technical requirements. It shall provide guards and a warehouse keeper then submit recommendations to the regional Police director to approve the license request.

- The license shall be issued by the regional Police director for a period not exceeding two years.

- Underground warehouses and processing workshop warehouses:

- The license shall be submitted to the Ministry represented by the regional Police (the Weapons and Explosives Department of the regional Police).

- The request shall be examined by a committee formed by a representative of the Weapons and Explosives Department of the regional police and a representative of the regional Investigations Department to ensure that it meets all the required conditions. The committee shall inspect the site on the spot to ensure that it meets all the required conditions and a warehouse keeper is available.

- The license shall be issued by the regional Police director and be valid for three years.

Chapter Three

Storage

Article Twenty-Eight:

Safety requirements to store explosives:

- Explosives shall be handed carefully and not thrown on the ground or handed roughly following the principles of care and caution.

- Storage shall be on a flat floor.

- Materials shall be stored on wooden pallets lifted from the ground by at least 10 cm.

- The height of the stack shall not exceed 180 cm and the width not more than 110 cm.

- The quantity of stored explosives shall not exceed two-thirds of the warehouse capacity.

- The distance between stacks shall be not less than 90 cm.

- Storage shall be in the designated areas.

- The distance between walls and stacks shall be not less than 90 cm.

- The warehouse shall be very clean and organized.

- Tags or labels shall be placed on the top of the stacks showing the type of explosives, date of manufacture, date of storage and the name of the project they are assigned to.

- It is not allowed to open and refill explosives boxes inside warehouses.

- Regarding the date of manufacture and storage, the oldest materials shall be withdrawn first.

- Check containers and pallets and replace the damaged ones.

- Explosives of different types shall not be combined together in the same warehouse (commit to explosives storage similarity).

- Detonators shall be stored in a separate warehouse from the other explosive materials.

- Any tools used to open the explosives boxes shall be made of wood, rubber or other materials that do not emit sparks, also, hammering shall be avoided when opening these boxes.

- Stored materials shall not be placed in the corridors and exits even temporarily.

- Comply with the manufacturer’s instructions in terms of (the stack height, temperature, coldness, humidity, ventilation and the expiry date).

- Metal warning signs shall be written clearly in Arabic and English, and placed in a visible place showing some instructions, such as "No Smoking", "No Open Flames" and "No Radio Transmitters".

- Machines and devices that emit sparks shall be away from the warehouse area. In addition, cleaning tools shall be of the type that does not emit sparks.

- Remove plants and grass in the warehouse area.

- Provide the warehouse with a thermometer and hygrometer.

- Warehouse and containers of flammable materials shall be away from explosives warehouses.

- Storing and withdrawing during rain, lightning and storms shall be prohibited.

- Make sure to close the electrical circuit of detonators during withdrawing them to any explosive project, whether using a standard factory closure or a manual one.

- Each establishment may store the quantities designated to more than one project inside one warehouse but within the capacity limits and the distance between each quantity to another shall not be less than 3 meters. The quantity designated to a specific project shall be previously stored in a specific place under a sign that shows the project name. Obvious partitions shall be placed between the quantities.

- Expired materials shall be isolated and reported immediately to the Department of Weapons and Explosives of the regional police to request destruction.

- When the warehouse needs repairs, the stored materials shall be transferred to another warehouse where safety and security requirements are applied.

Article Twenty-Nine:

Warehouse management rules:

- Any amount of explosives shall be withdrawn subject to a letter from the regional Police director (Weapons and Explosives Department).

- Withdrawal and entry of materials shall be carried out in the presence of the warehouse keeper and a regional police representative pursuant to a report of withdrawal and entry and under their responsibility.

- Explosive materials shall be stored with the approval of the regional Weapons and Explosives Director. The storage report shall be prepared by the warehouse keeper and the regional Police representative.

- Any warehouse shall not be opened except in the presence of both the police representative and the warehouse keeper.

- Each warehouse shall have two locks, one with the regional Police representative, and the other with the warehouse keeper. It is under their responsibility.

- No one shall be allowed to enter the warehouse without permission from the Weapons and Explosives Department.

Section Seven

Transfer

Based on Articles 4 and 10 of the Law, it is prohibited to transfer explosives except with the Ministry's permission and determination of conditions and procedures, technical and security specifications, and the safety requirements for explosives transfer and means of transport thereof.

Chapter One

Transfer conditions and requirements

Article Thirty:

Conditions and rules for explosives transfer:

- The explosives transfer form shall be filled out.

- The route of transportation means shall be determined.

- Provide necessary guarding.

- Relevant authorities shall be informed.

- It is prohibited to transfer explosive materials, according to the Hijri calendar, during the period from 30 of Dhu al-Qi'dah to 20 of Dhu al-Hijjah. But for both Makkah and Madina Regions, it is from 20 of Dhu al-Qi'dah to 25 of Dhu al-Hijjah.

- It is prohibited to transfer from warehouses to work sites where the distance is more than 150 km in rough mountain areas, and 300 km in other areas.

- In case of transit, the following is required:

- The competent authorities of both the source State and the destination State shall approve the transit.

- Determine explosives quantity, types and categories, in addition to the port of entry, port of exit, expected time, the arrival date of the shipment, names of drivers, copies of their passports, types of vehicles and the plate numbers.

- Specify the importer entity (the beneficiary), contact numbers and the full address.

- The Saudi Interpol shall be informed at least two weeks before the specified time of the shipment to transit Saudi Arabia's territories. It is unauthorized to transit during the Hajj season, which is set, according to the Hijri Calendar, from 30 of Dhu al-Qi'dah to 20 of Dhu al-Hijjah every Hijri year.

- The Public Security shall provide security guarding to transport the explosives since they enter Saudi Arabia territories until leaving.

- If the final destination of the shipment is one of the GCC Countries, the Customs fees shall be collected.

- Comply with security and safety requirements during explosives transfer.

- If the transfer to a warehouse located in another region of Saudi Arabia, the regional Police shall be informed of the date of transfer, quantity and the capacity of the warehouse where the explosive materials to be stored.

- Transfer fees shall be collected.

Article Thirty-One:

Security and safety requirements for explosives transfer:

- Explosives shall be transported by equipped transportation means and designed for this purpose. They shall never be transported by passenger transportation means.

- The highly sensitive explosive materials such as detonators shall not be transferred in one container with other explosive materials unless they are separated according to the carrier truck technical specifications.

- Any explosive materials shall not be placed in the truck cockpit.

- Unauthorized persons shall not be allowed to board the explosives carrier truck.

- The transported materials shall be well-placed to prevent moving and vibrating during transport.

- The transport means shall not have more than one trailer if it is a detachable type (truck and trailer), unless it is a train that is designated to transport explosive materials.

- Explosives carrier trucks shall avoid taking busy roads or downtown roads, and avoid rush hours.

- Explosives shall not be transported in heavy fog or rain, bad weather or sandstorms.

- The carrier truck loaded with explosives shall not be parked in populated areas, near bridges and tunnels, or in closed places such as garages.

- The speed of the explosives carrier truck shall not exceed 80% of the road speed limit. In any case, the speed limit of the carrier truck shall be 80 km.

- In case the explosives carriers drive in a convoy, the distance between each carrier and the other shall be at least 100 meters during driving, and at least 50 meters during stopping.

- When transporting explosives on long roads, two drivers shall take turns in driving the carrier truck.

- The driver shall be aware of the dangers of explosive materials and trained on how to deal with emergencies, fire and traffic accidents.

- Smoking shall be prohibited during loading and unloading, inside the carrier truck and around it in a distance not less than (30) meters.

- The carrier truck shall not carry any metal that emits sparks, flammable substances, acids or corrosive substances.

- The warning signs of danger shall be well placed on the carrier’s body, clean and clearly visible.

- Fire extinguishers shall be filled out, ready to use and easily accessible.

- Brakes, lights, horn, hazard lights, windshield wipers and tires shall be always safe and in perfect condition.

- An emergency repair kit shall be provided.

- The cockpit shall have written information about the dangers of explosive materials and emergency procedures in Arabic and English.

- The means of transport shall pass the Motor Vehicles Periodic Inspection every 6 months.

- The engine shall be turned off during loading, unloading or fueling up.

- The explosives carrier trucks shall be parked always in a proper position in order to move them easily and promptly in case of emergency.

- Loading and unloading shall be in an authorized place away from any source of flames and sparks.

- During loading and unloading, always turn the engine off, use the parking brake, use wheel stops and discharge static electricity.

- A warning triangle shall be used during emergency stopping in addition to red flags to warn pedestrians not to approach.

- In case of fire in the carrier truck, it shall be kept as far away as possible from populated areas and keep the truck away from the trailer and use fire extinguishers. But when the fire approaches the explosives container, fire shall not be resisted and immediately getaway, try to stop the traffic, evacuate the surrounding area for a distance of 600 square meters in all directions.

- The explosive materials shall be escorted by armed designated guards.

- The explosives carrier truck shall not stop after being loaded except in emergency situations.

- The carrier truckload shall not exceed the weight limit.

- The explosive materials shall be separated from ignition materials at a safe distance.

- The door lock keys of the materials carrier boxes shall be with the escort security man.

- Take the proper road.

- The transfer of explosives from a broken transportation means to another shall be prohibited until the General Department of Weapons and Explosives of the regional Police is informed.

- In case of any remarks, a report shall be prepared and handed over to the Department of Weapons and Explosives of the regional Police by the supervisor field Sergeant.

Chapter Two

Carrier specifications

Article Thirty-Tow:

Technical specification for the explosives carrier:

- The carrier shall conform to Saudi standards for transporting hazardous materials on roads.

- Take into consideration the manufacturer's instructions when making any modification or addition to the carrier, especially technical specifications such as total weight, dimensions, and so on.

- The carrier shall be strong enough to carry the load, in a good mechanical condition and its date of manufacture shall not be older than 10 years.

- Carry explosive materials in locked transfer containers designated for this purpose.

- The distance between the cockpit and the body of the carrier or container shall not be less than 15 cm.

- The carrier truck shall have dual rear wheels.

- The engine shall be diesel and located at the front of the carrier truck.

- The fuel tank shall be protected from damage and collision with solid and durable protectors totally away from the battery.

- The exhaust system shall have a noise damper, be away sufficiently from the fuel circuit, vertical and away from the body of the carrier truck.

- The electrical circuit shall be isolated and totally separated from the carrier body and container.

- The carrier truck shall have a protective rear bumper that protects the body in the event of a rear collision and about 15 cm from the rear of the truck.

- The carrier truck shall have an appropriate means of preventing static electricity.

- The carrier shall have a theft prevention system and a tracking system.

- The carrier truck shall a sufficient number of 10 kg fire extinguishers that use dry powder and easily to be used and accessed.

- The carrier truck shall have an emergency repair kit.

- Danger warning signs and stickers of the type that can be stuck and removed shall be placed on the carrier truck body.

- In case that the carrier consists of a truck and trailer, the connection between them shall be strong and quickly detached. The brake system shall control all wheels and have the ability to brake the trailer automatically when the connection lever gets broken.

- The container outer body shall be made of steel iron with a thickness of at least 2 mm or a layer of aluminum at least 4 mm thick. The celling shall be weaker than the sides.

- The container's inner body shall be lined with resistant wood at least 10 mm thick, including doors.

- The container doors shall be with two leaves that open to the outside and equipped with two strong locks.

- When designing a small container for detonators, it shall be placed between the cockpit and the main container. The steel iron of its walls shall not be less than 4 mm thick, and it shall be equipped with two strong and tight locks.

- The Department of Weapons and Explosives of the regional Police shall determine the technical specifications for the transportation means of oil well drilling pipelines which are equipped with explosives.

Section Eight

Usage

Based on Articles 4, 5, 6 and 10 of the Law, it is prohibited to use explosives without the Ministry's license and they shall not be used for anything other than the purpose for which the license is issued. The Regulations shall specify the conditions, procedures, technical and security specifications and safety requirements to be met when using explosives.

Chapter One

Construction

Article Thirty-Three:

Documents to be available to obtain a license for using explosives for construction purposes:

- A copy of a valid commercial register of the establishment or company and includes the activity of rock cutting.

- A copy of the blaster's license who will carry out the blasting so that the category of his license shall be not less than Class No. 1 if the project is inside the city, in addition to a copy of the work contract.

- A copy of the land property deed, the owner(s)'s IDs, the representation deeds, the representatives' IDs, the license of land grading, rock breaking or construction issued by the Municipality if the project is private.

- A letter of support from the relevant government entity supporting the license issuance of the project is governmental.

- A copy of the contract(s) that shows the relationship between the landowner or the project owner on the one hand, and the license applicant on the other hand.

- A sketch showing the borders of the land and the blasting sites is approved by an engineering office.

- A technical report issued by a consultant explaining the size and type of rocks to be removed, in addition to the blasting techniques and quantity needed.

- A written pledge by the license applicant to bear all damage sought from accidents related to the use of explosives approved by the Chamber of Commerce.

- Specific records for the company or establishment show the licensed quantity for projects and the actual blasted quantity.

- Provide any additional data or documents that the regional Police considers necessary to study the request.

Article Thirty-Four:

Conditions for license to use explosives for construction purposes:

- The applicant shall be the entity that will carry out the blasting whether the establishment/company contracting with the project owner or the sub-executing establishment/company.

- A project on-site report shall be prepared by the regional Police and relevant authorities (the government entity that owns the project if any, contractor, blaster, consultant office, and service agencies such as electricity, water and communications companies, if necessary). It shall show the site coordinates and how it is far away from residential areas, public facilities, roads and power lines. It shall prove that with pictures and recommend whether to use explosives in the project or not.

- Provide means to transport explosive materials in accordance with the Regulations.

- Provide all security and safety tools that are supposed to be used during blasting.

- If the project location is more than 150 km away from the warehouses of the company selling explosive materials in rugged mountainous areas and 300 km in other areas, it is required to build a temporary warehouse to store explosives in accordance with the Regulations or what the regional Police deems appropriate provided that it shall be checked by the regional Police prior to the license issuance. A report shall be made indicating the compliance with conditions, capacity, guarding and the manager requirements. Copies of the IDs and employment contracts of both guards and warehouse keeper shall be attached.

- If the project requires the demolition of an existing building, the use of explosives requires that other demolition methods cannot be used. Blasting shall be planned by senior and well-experienced blasters, in addition to providing sufficient guarantees to avoid any damage to others. Any senior blaster shall provide a CV showing his previous demolition works.

- The company or establishment that will carry out the project shall undertake to provide suitable housing for the project adjacent residents in case of evacuation.

- It is not permissible to issue a new license to use explosives at a site where a license has already been issued to use explosives in the same site except after terminating the previous license and settling the associated warehouse, if any.

- Commit not to use explosives in the Hajj season during the period from 30 Dhul-Qa`dah to 20 Duhl-Hajjah, and in specifically the Regions of Makkah and Al-Madinah during the period of 20 Dhul-Qa`dah to 25 Duhl-Hajjah as well as the month of Ramadan in central areas.

- Commit not to receive or use explosive materials without the supervision and control of the regional Police.

- Any additional requirements that the Public Security deems necessary for security and safety.

Chapter Two

Mines and Quarries

Article Thirty-Five:

Documents required to obtain a license to use explosives in mine and quarry works:

- A copy of the valid commercial register of the establishment or company that owns the project and a copy of it the commercial register of the executing contractor including the rock cutting activity, if there is an executing contractor.

- A copy of a valid exploitation permit issued by the Ministry of Petroleum and Mineral Resources.

- A copy of the blaster(s)'s license who will carry out the blasting works and a copy of their work contracts.

- A sketch shall show site borders and dimensions from residential areas and public roads.

- A technical report issued by a consulting agency shall include the size of rocks to be removed within two years, its quality, blasting technique and the amount of explosives needed.

- In case that the license applicant is the contractor, a copy of the contract signed by the project owner and the executing contractor shall be provided.

- A written undertaking by the license applicant to bear all damages resulting from any relevant accidents using explosives, whether casualty or property damages.

- Provide any additional data or documents that the regional Police deems necessary to study the request.

Article Thirty-Six:

Conditions for issuing a license to use explosives in mine and quarry works:

- The license applicant shall be the establishment or company that owns the project. The blasting executing contractor may request the license provided that the project does not have a permanent warehouse for explosives.

- A project on-site report shall be made by the regional Police and the relevant authorities (the project owner, the contractor and the blasting expert) that shows the site coordinates and matches its borders with the exploitation permission in addition to the recommendation to use explosives in the project or not, and quantity to be used.

- If the project location is more than 150 km away from the warehouses of the company selling explosive materials in rugged mountainous areas and 300 km in other areas, it is required to build a permanent or temporary warehouse to store explosives in accordance with the Regulations or what the regional Police deems appropriate provided that it shall be checked by the regional Police prior to the license issuance. A report shall be made indicating the compliance with conditions, capacity, guarding and the manager requirements. Copies of the IDs and employment contracts of both guards and warehouse keeper shall be attached.

- It is not permissible to issue a new license to use explosives at a site where a license has already been issued to use explosives in the same site except after terminating the previous license and settling the associated warehouse, if any.

- Commit not to use explosives in the Hajj season during the period from 30 Dhul-Qa`dah to 20 Duhl-Hajjah, and in specifically the Regions of Makkah and Al-Madinah during the period of 20 Dhul-Qa`dah to 25 Duhl-Hajjah as well as the month of Ramadan in central areas where quarries and stone factories are located. It is excepted that mines and cement companies can continue using only their stocks of explosives.

- Commit not to receive or use explosive materials without the supervision and control of the regional Police representative.

- Any additional requirements that the Public Security deems necessary for security and safety.

Chapter Three

Drilling of surface water wells

Article Thirty-Seven:

Documents required to obtain a license to use explosives in drilling surface water wells for citizens:

- A copy of the landowner's ID and a proof of ownership or a letter of support by the Emirate.

- The Ministry of Water's approval to drill the well at the specified location.

- A copy of a valid commercial register of the establishment or company that includes the activity of rock cutting if the owner agrees with it upon drilling the well.

- A copy of the blaster's valid license who will carry out the blasting.

- A copy of the contract signed by the well owner and the executing party, whether it is a blaster or a specialized establishment/company.

- A written undertaking by the license applicant, whether it is a blaster or a specialized establishment/company, to be responsible for all damages caused by any accident related to the use of explosives.

- Provide any additional data or documents that the regional Police deems necessary to study the request.

- An engineering consultant office shall estimate the necessary quantity of explosive materials and the quantity of rocks to be removed. Individual farmers are exempted from that in which that what is sent by the Ministry of Water shall be sufficient.

Article Thirty-Eight:

Conditions for issuing a license to use explosives in drilling surface water wells for citizens:

- The license applicant (the well owner) shall agree with the landowner or an establishment/company that its commercial register includes the activity of rock cutting.

- An on-site report on the well shall be made by the regional Police (Weapons and Explosives Department), the blaster and the well owner to determine dimensions, lengths and surroundings of the well.

- The explosive materials shall be given to the blaster according to the daily work need from the nearest warehouse owned by the selling company, and transported to the worksite even if the transfer distance exceeds 150 km in rugged mountainous areas and 300 km in other areas.

- The regional Police where the discharge warehouse is located shall escort the explosives and the blaster since taking them out until they are used and make any necessary reports.

- Commit not to use explosives in the Hajj season during the period from 30 Dhul-Qa`dah to 20 Duhl-Hajjah, and in specifically the Regions of Makkah and Al-Madinah during the period of 20 Dhul-Qa`dah to 25 Duhl-Hajjah.

- Any additional requirements that the Public Security deems necessary for security and safety.

Article Thirty-Nine:

Documents required for obtaining a license to use explosives in drilling surface water wells for government agencies (Ministry of Water and Electricity or Ministry of Agriculture):

- A copy of the valid commercial register of the establishment or company contracting with the government agency that includes the rock cutting activity.

- A copy of the blaster's license who will carry out the blasting works and a copy of its work contract.

- A copy of the contract concluded between the government agency and the contracted company or establishment.

- A letter of support from the relevant government agency addressed to the Department of Weapons and Explosives of the regional Police supporting the license issuance for the contracted company or establishment.

- A sketch showing the drilling sites of wells approved by an engineering office, and a technical report showing the size of the rocks to be removed.

- A written undertaking from the license applicant to bear all damages resulting from any accident related to the use of explosives.

- A written approval from the Ministry of Water or the Ministry of Agriculture.

- Provide any additional data or documents that the Department of Weapons and Explosives of the regional Police deems necessary to study the request.

Article Forty:

Conditions for issuing a license to use explosives in the work of drilling surface water wells for government agencies:

- The license applicant shall be the establishment or company that will carry out the blasting work.

- An on-site report on the wells shall be made by the regional Police and the relevant authorities such as (the government entity that owns the project, the contractor and the blaster), indicating the site coordinates and its distance from residential areas, public facilities, roads and power lines.

- Provide means of transportation for explosive materials according to the Regulations.

- Provide all security and safety tools to be used during blasting.

- If the project location is more than 150 km away from the warehouses of the company selling explosive materials in rugged mountainous areas and 300 km in other areas, it is required to build a temporary warehouse to store explosives in accordance with the Regulations, provided that it shall be checked by the regional Police prior to the license issuance. An inspection report shall be made indicating the compliance with conditions, capacity, guarding and the manager requirements. Copies of the IDs and employment contracts of both guards and warehouse keeper shall be attached.

- Commit not to receive and use explosive materials without supervision and control of the regional Police (Department of Weapons and Explosives).

- Commit not to use explosives during the Hajj season from 30 Dhul-Qa`dah to 20 Dhul-Hijjah, and in the two Regions of Makkah and Al-Medina during this period.

- Any additional requirements that the Public Security deems necessary for security and safety.

Chapter Four

Drilling of oil, gas and deep-water wells

Article Forty-One:

Documents required for obtaining a license to use explosives in drilling oil, gas and deep-water wells:

- A copy of a valid commercial register of the establishment or company executing the drilling works.

- A copy of the license to practice the activity of importing explosive materials issued by the Ministry (if any).

- A letter of support from the Ministry of Petroleum and Mineral Resources or the relevant government agency supporting the issuance of the necessary license.

- A sketch of the worksite and a report showing the expected volume of work.

- A written undertaking by the license applicant to bear all damages resulting from any accident related to the use of explosive materials.

- Provide any additional data or documents that the regional Police deems necessary to study the request.

Article Forty-Two:

Conditions for obtaining a license to use explosives in drilling oil, gas and deep-water wells:

- The license applicant shall be the establishment or company that will carry out the blasting through the drilling pipes.

- Provide suitable transportation means to transport drill pipes filled with explosives, in compliance with security and safety requirements, and as determined by the regional Police.

- If the project location is more than 150 km away from the warehouses of the company selling explosive materials in rugged mountainous areas and 300 km in other areas, it is required to build a temporary warehouse to store explosives in accordance with the Regulations, provided that it shall be checked by the regional Police prior to the license issuance. An inspection report shall be made indicating the compliance with conditions, capacity, guarding and the manager requirements. Copies of the IDs and employment contracts of both guards and warehouse keeper shall be attached.

- Provide all security and safety tools that are supposed to be used during blasting.

- Commit not to receive or use explosive materials without supervision and control of the regional Police.

- Any additional requirements that the Public Security deems necessary for security and safety.

Chapter Five

Seismic Survey (Seismology)

Article Forty-Three:

Documents required for obtaining a license to use explosives in exploration works (Seismic):

- A copy of a valid commercial register of the establishment or company that includes the rock cutting activity.

- A letter from the Saudi Arabian Oil Company (Saudi Aramco) proving that the land is within its concession or a valid copy of the exploitation permit issued by the competent ministry with submitting the original for authentication.

- A sketch of the site specifying the distance of the site from residential areas and public roads approved by an engineering office with specifying the coordinates.

- An approved technical report by a consultant, stating the exploration depth and the quantity and type of materials to be purchased.

- A copy of the contract(s) clarifying between the project owner and the executing entity.

- A written undertaking by the license applicant to bear all damages resulting from accidents related to the use of explosives, and it shall be certified by the Chamber of Commerce, or provide insurance for risks that may affect others.

- A copy of the blaster's license who will carry out blasting works.

- A written undertaking by the blaster to abide by the security orders and instructions during blasting and to provide the means of safety and security.

Article Forty-Four:

Conditions for obtaining a license to use explosives in seismic surveys (seismology):

- The license applicant shall be the establishment or company that owns the project or the blasting executing contractor.

- A project on-site report shall be made by the regional Police and the relevant authority (the project owner, the contractor and the blaster) indicating the coordinates of the site and matching its borders with the company’s concession or exploitation permit.

- If the project location is more than 150 km away from the warehouses of the company selling explosive materials in rugged mountainous areas and 300 km in other areas, it is required to build a permanent or temporary warehouse to store explosives in accordance with the Regulations, provided that it shall be checked by the regional Police prior to the license issuance. An inspection report shall be made indicating the compliance with conditions, capacity, guarding and the manager requirements. Copies of the IDs and employment contracts of both guards and warehouse keeper shall be attached.

- It is not permissible to issue a new license to use explosives at a site where a license has already been issued to use explosives in the same site except after terminating the previous license and settling the associated warehouse, if any.

- Commit not to receive or use explosive materials without supervision and control of the regional Police.

- Provide transportation means for explosive materials in accordance with the Regulations.

- Any additional requirements that the Public Security deems necessary for safety and security.

Chapter Six

Usage procedures

Article Forty-Five:

First: Procedures for obtaining a license to use explosives:

- The usage license application shall be submitted to the regional Police (Department of Weapons and Explosives), provided that the applicant's description matches the license type to be issued.

- The application shall be submitted to the Public Security after checking the documents and fulfilling all conditions.

- The license shall be issued by the Public Security for a maximum period of three years including (quantity and location) and is renewed for a similar period whenever the licensee complies with the usage regulating rules. In case the license is lost or damaged, it shall be replaced for the remaining period, including the same information.

- After the license is issued by the Public Security, the licensee shall apply to the regional Police (Department of Weapons and Explosives) to be allowed to purchase the quantity. The regional Police where the purchasing entity is located shall be notified, and the licensee shall comply with the withdrawal order issued for use.

- The ongoing licensees shall be obligated to reform their situation in accordance with the present Regulations within a period not exceeding one year from the issuance of the Regulations.

- The consuming importing entities (Aramco) shall be licensed without specifying the quantity.

- The Public Security may revoke the license if the conditions are not complied with, or when the security interest requires that.

Second: Procedures for withdrawing the licensed explosive materials:

- The company or establishment shall submit to the Department of Weapons and Explosives of the regional Police requesting to withdraw explosives on a daily basis for the project which was previously licensed. The request shall state the required quantity of explosive materials for one day only, and a declaration by the blaster confirming the readiness of the holes.

- The Department of Weapons and Explosives of the regional Police shall match the quantity written in the request with the records and write the appropriate quantity based on the project site importance.

- All daily requests shall be written in a list signed by the Weapons and Explosives Department of the regional Police.

- The list and withdrawal requests shall be sent to the sergeant in charge of the warehouse.

- The sergeant in charge of the warehouse shall ensure that the means of transport are in compliance with the technical and security specifications and the security and safety requirements provided for in the present Regulations.

- The quantity required for each project shall be withdrawn and handed over to both the accompanying security man and the blaster, and a withdrawing report shall be made.

- A blasting report and a declaration of blasting numbers, time and vibration degree that was carried out shall be sent by the blaster to the Department of Weapons and Explosives of the regional Police attaching a report on returning the remaining quantity, if any, to be written in the project records.

Third: Procedures for adding more quantity to the issued license:

- A letter by the licensee to the General Department of Weapons and Explosives of the regional Police specifying the quantity to be added to the project.

- A technical report includes the quantity to be added and the volume of rocks to be removed.

- A list of the licensed previous quantity specifying the quantity consumed, the remainder, and the quantity to be added.

- A project on-site report shall be made by the Department of Weapons and Explosives of the regional Police.

Fourth: Procedures for renewing the license:

- A letter from the licensee requesting the renewal of a license shall be submitted to the General Department of Weapons and Explosives of the regional Police.

- A list shows the basic (licensed) quantity, withdrawn and remaining quantity to be renewed.

- A consultant engineering report showing the volume of remaining rocks.

- A copy of the property deed with the original for authentication.

- A letter by the project owner stating his desire to continue working on the project.

- A copy of the explosive materials usage license to be renewed.

- A copy of a valid paving and crushing license.

Fifth: Procedures for license termination:

- A letter by the licensee shall be submitted to the General Department of Weapons and Explosives of the regional Police requesting the license to be terminated due to the end of work.

- A list shows the licensed quantity, used and remaining quantity (to be terminated).

- A copy of the usage license to be terminated.

- If the remaining quantity in the beneficiary company's warehouses is expired, they shall be destroyed.

- If the quantity is still valid, the specialists shall examine them and a record is prepared to return them to the seller's warehouses.

- Settle the records and add the returned quantity to the seller's warehouse.

Sixth: Rules of withdrawal and deduction of the quantity licensed for purchase:

- The license shall be registered in the company or establishment records held by the Weapons and Explosives Department of the regional Police.

- The company or establishment in charge of the project shall be notified by an official letter stating that the license is received and using the explosives is allowed.

- Licensed quantity shall be withdrawn daily.

- Deduction from the quantity shall be done according to the daily blasting report and recorded in the book records and computer.

- A statement showing the monthly data of every company or establishment shall be submitted to the General Department of Weapons and Explosives of the Public Security by the end of each month to state the withdrawn and remaining of the licensed quantity.

- A statement showing the withdrawn and remaining balance of the licensed quantity shall be prepared by end of the project.

- A letter shall be prepared to request the termination of the license and remaining quantity by the Public Security.

- Remarks shall be written on the project record margin after the termination order is received from the Public Security

- The company or establishment shall be notified through a letter of termination of the project.

Chapter Seven

Security and Safety Rules

Article Forty-Six:

Security and safety requirements for the use of explosives on site:

- Check location readiness before submitting the request and releasing quantities from the warehouse.

- Abide by the means of safety and security for staff on site.

- Wear the full uniform for blasters and on-site personnel.

- Blasting in bad weather conditions shall be prohibited.

- Be careful during unloading explosives from the means of transport.

- Ensure to make inventory during unloading on the site.

- Unauthorized persons shall not be allowed to access the site.

- Use blasting mats when necessary.

- Use a seismometer.

- Ensure that the site is evacuated.

- Alarm neighbors using a loudspeaker before blasting.

- Close all roads leading to the blasting site.

- Leave a safe and adequate distance for all away from the blasting site.

- Check the site after blasting and make sure that all blasting charges are blasted.

- Ensure to destroy blasting remnants.

- Make sure that the escorts are with the carriers by following them from warehouses till they arrive at the site.

- Ensure that the explosive materials carrier is properly parked at the site, the doors are locked with locks and the escorting security officer has the key.

- Ensure that the escorting person is at the appropriate location to ensure that the explosive materials are guarded.

- Ensure the availability of security and safety means at the blasting site (adequate blasting mats, seismograph, the truck that lifts and places the blasting mats, blasting battery and voltmeter).

- Ensure that on-site blasting devices are ready.

- Ensure that explosive materials are used in the project for which they were withdrawn.

- Ensure that workers at the site are licensed to work.

- Make sure that the blaster is in the blasting field and doing the work himself.

- Attendance at the site shall be before the blasting time, especially at locations where the nearby roads have to be closed.

- If there are near roads that need to be closed, a traffic patrol shall be ordered before blasting.

- Make sure of the number of blasting determined for the projects.

- Move quickly in the event of an accident at any of the blasting sites, and call the management simultaneously.

- Ensure that sites are cleared of workers, cars and pedestrians before blasting and nearby roads shall be closed.

- Make sure of surveying the site after blasting.

- A daily report shall be prepared according to the approved form for each site and submitted to the Weapons and Explosives Department of the regional Police.

- Ensure the availability of security and safety requirements in the explosive carrier before arriving at the warehouse.

- Escort of quantity as the blaster transports them.

- Smoking shall be prohibited in warehouses, during transport or at the blasting site.

- Disconnect all means of communication at the blasting site.

- Ensure that workers in the blasting site are licensed.

- Unlicensed persons shall not have access to the blasting site.

- Ensure the integrity of the holes and the angle of inclination.

- The blaster shall charge the holes with explosive materials, connect and check the electrical circuit.

- Do not rely on workers to charge the holes with explosives and connect detonators.

- Do not destroy any extra quantity of explosive materials and tools.

- Return any extra quantity of explosive materials and tools to the warehouse and prepare a return report.

‏Section Nine

‏Guarding of Explosives

Based on Articles 8 and 10 of the Regulations, it is prohibited to seek assistance of personnel or guards of security companies to perform the work of guarding explosives without the Ministry's permission. The Regulations shall determine the conditions and procedures to be fulfilled for guarding of explosives and the persons in charge of guarding.

‏Chapter One

Article Forty-Seven:

Conditions for explosive guards:

- Guards shall be military personnel and working for companies authorized to guard civilian explosives.

- Guards shall be Saudi citizens for those who work for authorized security companies.

- He shall have no criminal or security record.

- He shall be physically and mentally healthy.

- He shall pass the drug test.

- He shall be 25 to 50 years old.

- He shall have a training course on the security and safety of explosives.

Chapter Two

Article Forty-Eight:

‏Procedures and rules for explosives guarding:

- Explosive guards shall be military and armed.

- Civilian guards authorized by the Ministry of Interior may be hired.

- Guarding the explosives and fireworks production and storage sites shall be all the time.

- In case of the use of civilian guards, it shall under the supervision of the competent authority (Department of Weapons and Explosives of the regional Police).

- Guard explosive materials during transport and use at worksites.

- The competent authority (Department of Weapons and Explosives of the regional Police) shall control production, warehouses and project sites through the surveillance room equipped with 24-hour memory drives and cameras and provide anti-theft and fire systems.

- The period of guarding the explosives at blasting sites shall be from the time of receiving the explosives until the completion of the field survey.

Section Ten

Explosive Technicians and Professionals

Based on Articles 9 and 10 of the Regulations, unauthorized persons may not engage in or supervise blasting works. The Regulations shall set out the technical, security and safety requirements, procedures and security specifications for blasting technicians and explosive professionals.

‏Chapter One

License

Article Forty-Nine:

Conditions for the applicant of explosive technician license:

- He shall be a Saudi citizen.

- He shall have an academic degree no less than high school.

- He shall not be convicted for a crime against immoral behavior and breach of trust.

- He shall be at least 21 years old.

- He shall have a medical certificate proving that he is free from any physical and mental diseases, and fitting to work as a blaster.

- He shall pass the drug test.

- He shall have carried out blasting works for at least six months and he is knowledgeable and skillful in blasting work.

- He shall pass a training course of at least two weeks from an accredited institution.

- A written request for a civilian blasting training course shall be submitted.

- The applicant shall pass the security screening.

- He shall pass the personal interview and the theoretical and practical test.

Article Fifty:

Conditions for being a warehouse keeper:

- He shall be a Saudi citizen.

- He shall have no criminal or security record.

- He shall be at least 25 years old.

- He shall pass the drug test.

- He shall have no less than a high school degree.

- He shall pass a training course on the management of explosives warehouses from a specialized company.

- He shall work for the authorized company.

- He shall have a computer training course.

Article Fifty-One:

Conditions for the driver of the explosives truck carrier:

- He shall be a Saudi citizen if possible, or a worker under the sponsorship of the project owner or the carrier establishment.

- He shall have a driving license (public).

- He shall be at least 25 years old.

- He shall have no criminal or security record.

- He shall pass the drug test.

Article Fifty-Two:

Conditions for worker of loading, unloading and charging holes:

- He shall be a Saudi citizen if possible, or a worker under the sponsorship of the project owner or the carrier establishment.

- He shall have no criminal or security record.

- He shall be physically and mentally healthy.

Article Fifty-Three:

Procedures for obtaining a blasting technician license:

- A license application shall be submitted to the Ministry, represented by the Public Security and the regional Police, attached with the following:

- A clear copy of the national ID.

- A copy of the academic degree.

- A copy of certificates of any explosives training courses, if any.

- A print from the Civil Affairs proving that he does not work for any government sector.

- 6 recent color photos of the applicant, size 6x4 cm.

- A document proving that there is no criminal record.

- Once the documents and requirements are checked, the application shall be submitted to the Public Security.

- The license shall be issued by the Public Security (General Department of Weapons and Explosives) for a period of three years.

- Ongoing licensees shall be required to reform their situation in accordance with the present Regulations within a period not exceeding one year from the date of issuance of the Regulations.

- In order to renew the license for a period similar to the categories specified in Paragraphs 2 and 3 of Article Fifty-Four, the following conditions shall be met:

- Attach a no criminal record certificate.

- The applicant shall be physically and mentally healthy.

- He shall pass the drug test.

- He shall pass the security screening.

Article Fifty-Four:

‏Blaster license categories:

  - A trainee's license is granted during the training period to those who wish to practice blasting and crushing rock works.

  - Blaster license outside cities, category 2.

  - Blaster license inside cities, category 1.

‏Article Fifty-Five:

Request to amend the blasting license category two to category one:

- Pass the scientific test with at least 90 marks.

- Do not apply until two years after the date of obtaining the category two license passed.

- Attach a practice proof from the establishment or company that he worked for during the past two years indicating the periods of practice and the number of blasting operations he carried out and how they were far away from houses, facilities and so on. Also, it shall prove that he is knowledgeable and skillful in careful blasting techniques.

- Attach the origin of the previous license.

- He shall be practically tested in careful blasting techniques, bases and technical rules.

- Form a committee of (Department of Weapons and Explosives of the regional Police by two members, an experienced blaster and a member of the companies specialized in manufacturing explosives) to conduct the test.

Section Eleven

Training

Based on Article 4 of the Law, it is prohibited to attend training in explosives except with the Ministry's license in accordance with the provisions of the Law and its Regulations.

Chapter One

License

Article Fifty-Six:

Procedures for obtaining a license:

  - The application for a license in the field of explosives shall be submitted to the General Department of Weapons and Explosives of the Public Security.

  - The application shall include the names of trainers and trainees, the training program, the place of course and the training date.

  - The request shall be studied by the General Department of Weapons and Explosives of the Public Security.

  - After the request is approved, the Director of Public Security shall issue the license.

Chapter Two

Conditions of trainer and trainee

Article Fifty-Seven:

Conditions to be met by the trainer:

    - He shall have a high degree or advanced studies in the field of explosives engineering, mining, geology or chemical engineering.

    - The applicant shall have previous field experience in blasting works for an appropriate period.

    - He shall have previously presented courses in blasting techniques and works.

    - He shall belong to or work through a manufacturing company that has a special training license.

    - The applicant shall have the basic skills and ability to communicate with the trainees.

    - He shall have the presentation skills to attract trainees to actively participate in training by motivating them skillfully to ask and discuss.

    - He shall have good preparation skills for lectures and to master presentations using modern presentation aids.

Article Fifty-Eight:

Conditions to be met by the trainee:

- He shall be a Saudi citizen in case that the course is to prepare blasters. But in other courses, other persons are allowed.

- The trainee shall be at least 25 years old.

- The trainee shall pass the security screening and medical examination.

- The trainee shall not have a criminal or security record.

- He shall be adequately educated to understand and perform blasting work.

- It is preferable that the trainee has basic skills in using computers and reporting.

- He shall belong to one of the entities that carry out blasting, security entity, military entity or any relevant entity. Trainees in training of blasters courses are excepted.

Chapter Three

Subjects and Scope of Training

Article Fifty-Nine:

Subjects of training:

- The origin of civilian explosives.

- Ignition systems.

- Drilling.

- Warehouses.

- Safety at work sites.

- Rules and conditions of warehouse guarding.

- Rules to guard and transport explosives to blasting sites.

- Duties of security supervisors over blasting works.

- Control the movement of warehouses (incoming, outgoing, remaining and daily and monthly inventory).

- Reduce the vibrations resulting from blasting.

- crush rocks as efficiently as possible.

- Increase the blasting efficiency.

- Blasting works in mines.

- Demolition works.

- Environment-friendly technologies.

- Security and safety measures in transporting and storing explosives and dealing with them in case of emergency.

Article Sixty:

Training course curriculum:

- Covers the basic topics of explosives and means and techniques of ignition (electric, non-electric).

- Covers the scientific, engineering and technological aspects in the field of blasting (drilling, explosives charging and ignition).

- Includes the use of computer applications in design and blasting operations.

- Consists of security, safety and environmental aspects regarding all blasting works.

- Includes some aspects of transporting, storing and disposal of explosives in accordance with international standards, and safe handling in case of emergency.

- Executes theoretical and practical applications on how to design and carry out blasting works and submit written reports and verbal presentations.

- Tasks trainees to use databases and international references to get updated in the field of blasting.

- Covers administrative aspects related to the roles of all parties involved in blasting works.

- Covers any updates in explosives science.

Article Sixty-One:

Requirements for preparing course programs:

- Determines the course name, technical level, duration, place and number of trainees.

- Prepares the training curriculum (hour, day, week and month).

- Prepares a training program showing the subject, the duration in hours, the trainer name and training aids.

- Prepares the scientific content and a list of reference names needed by trainees and how to access them.

- Equips training rooms with training aids that enable trainees to understand.

- Allocates hours for practical training and prepares theoretical applications and reports.

- Allocates hours to present reports verbally.

- Determines the time of theoretical and practical exams and shows how the evaluation marks are divided.

Section Twelve

Ceding

Based on Articles 5 and 10 of the Law, explosives may not be ceded or disposed of, except with the Ministry's permission. The Regulations shall specify the conditions and procedures for doing so.

Article Sixty-Two:

Conditions to cede explosives:

- The company ceded for shall have a valid license.

- Both ceding and ceded for companies shall agree upon that.

- Ceding shall be limited to oil well drilling companies.

- The ceded explosive materials shall be usable and unexpired.

- The company ceded for shall have legal warehouses.

- If the company that owns the explosive materials wishes to transfer the materials to another license, that license shall be valid.

Article Sixty-Three:

Procedures of ceding:

  - The beneficiary entity shall apply for ceding to the Department of Weapons and Explosives of the regional Police attaching the following:

    - A valid license for both the company ceded for and the ceding beneficiary.

    - A written consent of the company ceded for.

    - Attach a report proving the validity of explosive materials for use.

    - A letter pledging to be liable for all damages resulting from use.

  - After completing the conditions and procedures, the Department of Weapons and Explosives of the Public Security shall issue the ceding license.

Section Thirteen

Destruction

Based on Articles 4 and 10 of the Law, it is prohibited to destroy explosives except with the Ministry's permission. The Regulations shall specify the conditions, procedures, technical specifications, security and safety requirements when destroying them.

Chapter One

Conditions and Procedures

Article Sixty-Four:

Conditions for explosives destruction:

- Clarify the main justification for taking action to destroy.

- Determine the type and quantity of materials to be destroyed.

- Locate a suitable site that has already been prepared for destroying explosive materials and their accessories.

- Prove the destruction by video camera and photography in addition to reporting.

- Determine the appropriate way to destroy the materials by the blaster.

Article Sixty-Five:

Procedures for destroying explosives:

- Any entity that has explosive quantity shall inventory them and submit to the Weapons and Explosives Department of the regional Police to request approval for destruction.

- The Weapons and Explosives Department of the regional Police, after the destruction request is approved, shall determine the destruction date and notify the company of that to bring a blaster who is experienced in destruction. The blaster shall have a blasting license or being an oil wells blasting engineer, as well as provide suitable transportation means.

- The quantity to be destroyed shall be released on the day of destruction in the presence of a committee formed by the Weapons and Explosives Department representative, the company representative, a blasting expert and the beneficiary representative.

- The quantity shall be transported to the designated place then destroyed. The procedures and conditions for the transfer stipulated in the Regulations shall apply.

- After destruction, the committee that carried out the destruction shall prepare a destruction report.

- The destruction site shall be cleaned of any residue of explosive materials.

- The destruction of explosive materials in factories where it happens continuously shall be carried out subject to a report from the Weapons and Explosives Department of the regional Police.

Chapter Two

Section Fourteen

Fees

Based on Article 29 of the Law, the Regulations shall determine the financial fees for the services provided by the Ministry to guard explosives during transport, storage or use, provided that quantity and distance shall be taken into account when determining the fees.

Article Sixty-Six:

Rules of the collection of financial fees for guarding explosives:

  - Fees shall be collected for the following explosive materials products (ANFO explosives, emulsion explosives, electric detonators and non-electric detonators).

  - Fees for the above-mentioned explosive materials shall be collected when they are taken out from a central warehouse pursuant to a releasing report according to the following pricing:

    - Twenty Halalas for each detonator.

    - Ten Halalas for each kilogram.

    - Five Halalas for each detonation cord meter.

  - The financial fees shall be calculated when the manufacturer applies to the regional Police for security escorts in preparation to take out the explosives and transfer them from central warehouses to beneficiaries.

  - Fees shall be calculated based on a form that determines the due amount and signed by the manufacturer and the regional Police. This form shall have a unique serial number and be distributed in three copies, one for the company, another for the Public Security and the last for the Ministry.

  - The manufacturer shall pay within one month as maximum from the date of releasing the quantity. Payment shall be deposited in the Ministry's bank account referring to the form serial number in order to facilitate the follow-up and control process.

  - In the event that manufacturers are late in paying the dues, the bank guarantees provided by them to obtain the manufacturing license shall be used to pay any overdue amounts.

  - Financial fees shall not be amended or refunded for the return of extra quantity or any other reason.

Section Fifteen

Exemption from Penalty

Based on Article 26 of the Law, the Regulations shall specify the rules for exemption from penalties stipulated in Articles 15, 16, 17 and 21 for everyone who takes the initiative to report to authorities any violation before or after it occurs.

Article Sixty-Seven:

Rules for exempting the offender from penalty in case of the initiative to report the violation after occurrence:

- The offender shall not have been previously sentenced and repeats the same violation.

- The report shall be made before the security authorities know about the violation and related damage.

Violators shall be exempted from the penalties stipulated in Article 26 in accordance with the following rules:

- If the report is made before committing the violation, it shall be before the authorities know about it.

- If the report is made after committing the violation, this report shall have assisted in arresting the partners in the same violation, or in another violation similar in type and seriousness, or that committing the violation does not harm others.

- The reporter shall not incite committing the violation.

Section Sixteen

Permanent Committee

Article Sixty-Eight:

The committee shall be formed by the Minister's decision and headed by the General Department of Weapons and Explosives and the membership of (General Investigation, Public Security and General Secretariat of the High Commission for Industrial Security) to study license requests for the manufacture, import and export of explosives and to ensure that the required conditions are met. The committee shall have the right to except from the conditions and rules set forth in the Regulations after the Minister's approval subject to security interests.

Section Seventeen

Fireworks

Based on Articles 9 and 10 of the Law, unauthorized persons may not operate fireworks devices. The Regulations shall specify the conditions, procedures, technical and security specifications, and safety requirements for storing and transporting fireworks, preparing fireworks displays and places, and who are authorized to operate them.

Chapter One

License

Article Sixty-Nine:

- The applicant shall be a Saudi citizen.

- He shall have a valid commercial register.

- He shall have no security restrictions.

- Commit to security and safety procedures and requirements when transporting, storing, and executing displays.

- The applicant shall have a bank guarantee or insurance from one of the insurance companies in Saudi Arabia to cover workers and third parties.

- Provide special trucks to transport fireworks according to the specifications set by the Regulations.

- Provide permanent warehouses for storing fireworks according to the conditions and specifications set by the Regulations.

- Provide a full computer system to control inventory.

Article Seventy:

Procedures for obtaining a license to import fireworks:

- The license request shall be submitted to the Ministry, represented by the General Department of Weapons and Explosives, attached with the following:

- A true certified copy of the license applicant ID.

- A copy of the commercial register.

- A copy of the bank guarantee or insurance.

- A written declaration stating that the applicant is informed of conditions and rules for practicing the activity.

- A written undertaking not to sell or dispose of fireworks to anybody wishing to do fireworks displays until being approved by the General Department of Weapons and Explosives of the regional Police.

- The request shall be examined by the Department of Weapons and Explosives of the regional Police to ensure that it meets all the required conditions. The recommendation is submitted to the Minister to be approved or refused.

- After the Minister's approval, the license shall be issued for a period of three years, and shall be renewed for a similar period when the licensee complies with the activity regulations. In the event of the license loss or damage, it shall be replaced for the remainder period using the same information.

Article Seventy-One:

Procedures for fireworks displays:

First: Anybody who wishes to arrange for fireworks displays shall formally apply to the Emirate of the region at least 45 days prior to the display date. The display place and time as well as the executing entity shall be determined. The following shall be attached to the request:

- A copy of the fireworks operating activity license of the display executing entity.

- Locate the coordinates of the fireworks display site.

- Determine the fireworks supplier and the port of arrival if the contractor is from abroad.

- A written consent by the landowner on which the fireworks display will be held, if necessary, according to the estimates of the Weapons and Explosives Department of the regional Police.

- A written declaration by the performing entity to comply with the conditions and rules of executing fireworks displays.

- A list of fireworks to be used in the display by using the form No. 2 which includes:

- Type and class of fireworks to be used in the display (use technical terms).

- The United Nations number and risk level.

- Quantity and weight of each unit and the total weight of the whole quantity.

- Fireworks projectile height range.

Second: Fireworks shall be launched electronically, and traditional launching is not allowed.

Third: After approval, the request shall be referred to the regional Police to complete the procedures and take the necessary measures to check the site, with the participation of the regional Civil Defense to ensure that the site is proper for display and a joint report shall be done with the executing entity.

Fourth: After completing the required procedures, the display license shall be issued and signed by the Director of Public Security or his representative indicating the place and time of the celebration, the executing entity and the quantity to be released. A copy of this license shall be sent to the Ministry of Health, Civil Defense, General Investigation, Saudi Red Crescent Authority and Customs in which that each authority shall take the necessary procedures of its competence.

Fifth: The Department of Weapons and Explosives of the regional Police shall determine which relevant authorities are to be present at the display place. Both Civil Defense and Red Crescent shall be present in all cases.

Sixth: the licensed quantity shall be used for the purpose for which the license was issued.

Chapter Two

Security and Safety Rules

Article Seventy-Two:

Security and safety rules that shall be met during fireworks displays:

First: The Civil Defense Department shall take the following steps:

- Make sure that the display equipment (launchers and others) is safely far away from spectators, residential areas, parking lots, health care areas, prisons, hazardous materials storage areas, fuel stations, power plants, transmission towers, factories and commercial centers. In addition, the potential position where the projectile falls shall be safely far away from the said areas and places.

- Make sure that the projectile trajectory is clear of any obstacles in all directions.

- Ensure that adequate equipment is in place for intervention when needed. Appropriate means of protection such as equipment and others shall be available depending on the territorial nature to ensure public safety.

- Immediately halt the display when the wind direction or speed change to a degree that, according to the recommendation of the Civil Defense representative, leads to an obvious danger, so the display is delayed until weather conditions are improved. It shall be halted too when spectators become out of control.

Second: The Department of Weapons and Explosives of the regional Police shall take the following procedures:

- Prohibit the use of wireless devices and mobile phones near electrical detonators within a distance of 15 meters.

- Prohibit the use of batteries and exposed wires during the launching process when an electrical control box is used that is powered by a detachable switch breaker and equipped with buttons connected to electrical wires.

- A delay device shall be used for a sufficient safety period that is giving the same duration to give the fireworks operator enough time to move away when fireworks are launched manually.

- Smoking shall be strictly prohibited before, during and after fireworks launching.

- Prohibit igniting any kind of flame or smoking in fireworks shells storage sites, or in or near the launch area, or any of its components. Operators and their assistants shall use safe lighting methods, such as portable torches or non-flammable electric lights (not incandescent). In addition, place clear guiding signs in both Arabic and English in this regard and provide automatic and manual tools for detection, surveillance and firefighting.

- The regional Police shall deploy a sufficient force around the display area (launching).

- The Department of Weapons and Explosives of the regional Police shall provide the General Department of Weapons and Explosives of the Public Security with consuming reports which show that all imported quantities have been consumed in addition to giving their opinions regarding the display operating entity.

Third: Security and safety rules that shall be met during fireworks displays launched from the top of buildings or facilities:

- Cover all AC units on building roofs used for launching and surrounding buildings, according to the estimates of the General Department of Weapons and Explosives of the regional Police, in coordination with the Civil Defense Department to prevent the access or entry of fireworks launching residues.

- Spectators shall not be allowed to be on the roof of buildings used for launching or on the roof of surrounding buildings.

- It is not allowed to have flammable materials or drying clothes on the roof of buildings used for launching or on the roof of surrounding buildings.

- Close all windows of the used building and the surrounding buildings during the display duration.

- Fireworks shall not be launched from building roofs with more than 25 meters high.

- Commit to any other instructions that the Public Security deems necessary.

Fourth: Both the display owner and operator shall inventory all shells that fail to ignite or are improper for launching, and submit a statement on that to the specialists of the Weapons and Explosives Department on site to be destroyed.

Fifth: The Saudi Red Crescent Authority shall provide the necessary first aid and medical services at the display site.

Chapter Three

Fireworks Operator

Article Seventy-Three:

Conditions for obtaining a fireworks operator license:

• The applicant shall be Saudi, but the General Department of Weapons and Explosives of the regional Police may give exceptions regarding this condition according to their assessment.

• He shall be healthy and fit.

• He shall have no security restrictions.

• He shall have an accredited training certificate.

Article Seventy-Four:

Fireworks operator responsibilities:

First: Before display:

- Loads fireworks from warehouses into the transportation means and unloads them at the display site.

- Observes safety distances and secures the site.

- Examines all fireworks visually before use to ensure their validity and does not use any broken or damaged fireworks.

- Installs tightly the fireworks mortar tubes and directs them correctly to ensure that the projectile trajectory and shrapnel are within the ban zone.

- Installs and prepares fireworks for the display.

- Determines the fireworks projectile trajectory and makes sure that it is safe and free of any obstacles.

- Adheres to all security and technical directives and instructions, and security and safety procedures imposed by the fireworks manufacturer.

- Covers the holes of fireworks mortar tubes with light covering to make sure that the shell is out or not.

- Ensures that the shell is in contact with the bottom of the fireworks mortar tube, provided that it is not allowed to charge more than one shell in one tube at the same time.

Second: During displays:

- Supervises and controls all switches and means of triggering fireworks at all times to prevent and avoid their being launched by an unauthorized person or accidental launching.

- Halts the fireworks operation at any time when it is not safe to continue, or when the Weapons and Explosives Department of the regional Police orders to halt the display.

- Ensures that all fireworks are directed at a safe angle to ensure that they explode far from spectators and to ensure that none of their remnants and shrapnel fall outside the explosion zone.

- Examines the fireworks mortar tubes to ensure that they are fit and free of any residues before charging them with the proper shells.

- Prohibits igniting fireworks at all using lighters, matches or any other old means of ignition.

- Directs the fireworks launching at the predetermined and agreed-upon directions.

Third: After displays:

- Returns the remaining unused quantity to the warehouse under the supervision of the General Department of Weapons and Explosives of the regional Police.

- Inspects the launching site and the surrounding area after the display and collects any fireworks that may have failed to ignite and neutralizes them in preparation for destruction.

- Waits a period of at least half an hour starting from the end of the display, before allowing anyone to enter the launching site.

- Destroys all fireworks boxes and empty accessories to ensure that they are not used for other purposes.

Section Eighteen

Transport of Fireworks

Based on Articles 4 and 10 of the Law, it is prohibited to transport fireworks except with the Ministry's license. The Regulations shall specify conditions, procedures and requirements for security and safety during transport.

Chapter One

Transport Conditions and Requirements

Article Seventy-Five:

Conditions for transporting fireworks:

- Fill out the fireworks transport form.

- Specify the route.

- Provide the necessary guarding.

- Inform the relevant authorities.

- When transporting in transit, the competent authorities' approval of both the state of origin and the state of destination shall be obtained.  The conditions of transit referred to in Paragraph 7 of Article Thirty of the present Regulations shall be observed.

- If the transport is to a warehouse located in another region, the regional Police shall be notified of the transport date, quantity and the warehouse capacity in which the fireworks are to be stored.

Article Seventy-Six:

Security and safety requirements for the transport of fireworks:

The security and safety requirements shall be complied with when transporting fireworks, in accordance with Article Thirty-First of Section Seven regarding the security and safety requirements for transporting explosives.

Chapter Two

Carrier Specifications

Article Seventy-Seven:

The technical specifications of the fireworks carrier shall be adhered to in accordance with Article Thirty-Second of Section Seven relating to the technical specifications of the explosives carrier.

Section Nineteen

Storage of Fireworks

Based on Articles 4 and 10 of the Regulations, it is prohibited to store fireworks except with the Ministry's license. The Regulations shall specify the conditions, procedures and requirements of security and safety during storage.

Chapter One

Technical and Security Specifications

Article Seventy-Eight:

Those who are authorized to import fireworks shall store fireworks in permanent warehouses. If the importer imports fireworks for the purpose of occasional fireworks displays at specific times, he shall provide temporary warehouses. The technical and security specifications of constructing permanent and temporary warehouses shall be complied with.

Chapter Two

License

Article Seventy-Nine:

Procedures for obtaining a license to construct temporary warehouses:

The procedures mentioned in Paragraph 3 of Article Twenty-Seven of Section Six shall be complied with when constructing temporary warehouses.

Chapter Three

Safety Requirements

Article Eighty:

Safety requirements of fireworks storage:

The safety requirements mentioned in Article Twenty-Eight of Section Six shall be complied with when storing fireworks.

Section Twenty

Destruction of Fireworks

Based on Article 4 of the Law, it is prohibited to destroy fireworks except with the Ministry's license.

Article Eighty-First:

Conditions of fireworks destruction:

- Clarify the main reason for destruction.

- Determine the type and quantity of fireworks to be destroyed.

- Choose a proper site that is previously prepared for destroying fireworks and their accessories.

- Prove the destruction by video camera and photography in addition to reporting.

- Determine the appropriate technique for destruction.

Article Eighty-Two:

Procedures of destroying licensed fireworks:

- Any entity that has fireworks shall inventory them and submit a destruction request to the Weapons and Explosives Department of the regional Police.

- The Weapons and Explosives Department of the regional Police, after the destruction request is approved, shall determine the destruction date and notify the company or establishment of that to bring an operating technician who is experienced in destruction. He shall have a fireworks operator license, and suitable transportation means shall be provided.

- The quantity to be destroyed shall be released on the day of destruction in the presence of a committee formed by the Weapons and Explosives Department representative, Civil Defense, the company representative and the fireworks operator.

- The quantity shall be transported to the designated place then destroyed. The procedures and conditions of the transfer stipulated in the Regulations shall apply.

- After destruction, the committee that carried out the destruction shall prepare a destruction report.

- The destruction site shall be cleaned of any fireworks residue.

Section Twenty-One

General Provisions

Article Eighty-Three:

Companies that manufacture, import and export explosives, companies and establishments licensed to use explosives for various activities, as well as those holding licenses to transport explosives, in addition to citizens licensed to be blasting technicians shall be obligated to reform their status in accordance with the present Regulations within a period of one year from the date of the Regulations issuance.